SpaceWire-CPU-Interface Manual (v.1.0 Beta, Rev. 64)

1. Memory-Mapped IO
The SpaceWire Link Interface is split up into three sections: Transmitting (TX),	Receiving (RX) and Register (REG). Each one is, in an ARM-AXI based Memory-	Mapped Interface with 32-bit word width and address width, assigned to its own offset	address. Furthermore there are two ports, accessible via GPIOs, which are used to	control the logic reset as well as the transmitting of Time-Codes. Additionally, in case of	incoming Time-Codes, completed packages or status changes of the link, there is the	possibility to inform the CPU via interrupt signals.

1.1. Transmitting (TX)
Offset_TX + 0x0000_0000 : Address of transmit FIFO (write-only)
Offset_TX + 0x0000_0004 : Number of free FIFO spaces (read-only)

1.2. Receiving (RX)
Offset_RX + 0x0000_0000 : Address of receive FIFO (read-only)
Offset_RX + 0x0000_0004 : Number of available elements in RX-FIFO (read-only)

1.3. Register (REG)
Offset_REG + 0x0000_0000 : Link Configuration (read/write)
Offset_REG + 0x0000_0004 : Transmit Rate (read/write)
Offset_REG + 0x0000_0008 : Time-Codes (outgoing) (read/write)
Offset_REG + 0x0000_000C : Time-Codes (incoming) (read-only)
Offset_REG + 0x0000_0010 : Link-Status (read-only)

2. Memory Access
The Management and access of the transmit resp. receive functionality is done via the	AXI4-Full-Interface. The registers, however, are accessed via a AXI4-Lite-Interface. The	fundamental difference is that the Full-Interface supports burst transfers while the Lite-	Interface is only capable of doing single transfers and is therefore slower.

2.1. Transmitting (TX)
To write data into the transmit-FIFO the under 1.1. specified address must be the	destination address of a write request. When using burst transfers it is important to	ensure that the address is not incremented but remains constant (fixed burst). (See 4.2.)

2.2. Receiving (RX)
To read data from the receive-FIFO, the under 1.2. specified address must be the	source address of a read request. When using burst transfer it is important to ensure	that the source address is not incremented but remains constant (fixed burst).

2.3. Register (REG)
Access to a single register are possible with a single read/write request and the specific	using of the destination/source address. The configuration does not allow to overwrite	read-only registers by mistake so it is not necessary to take special care.

3. Technical Specification
In the following section the elements specified under 1. are described in more detail.

3.1. Transmitting (TX)
Data which is written into the transmit FIFO are gradually sent through a running Link-	Interface (See 2.1.). Is the interface in a non-connected state the data within the FIFO	are gathered and sent as soon as a connection attempt of the interface was successful.

The FIFOs width is nine bits wide which are divided as follows:
Bit 8 : flag bit (1: EOP/EEP, 0 : Data)
Bit 7 – Bit 0 : byte to send (0x00 for EOP, 0x01 for EEP)

In depth, 2049 records fit into the FIFO. Is the FIFO completely full and is then a write	request followed by a read request executed, the write request may fail. This is due to	technical reasons and can be circumvented by assuming the depth of the FIFO to be	one less than actual.

Data larger than 9 bits sent to the FIFO are ignored and not written into the memory. An	ultimately valid data transfer looks like this: 0x0000_0xvv, where x can be either 0x0 or	0x1 and vv any data byte. Is x equal to 0x1 and vv unequal to 0x00 or 0x01 the record	is ignored and not sent by the Link-Interface.

The TX-FIFO can be reset via the CPU (axi reset). Thereby the FIFO is pseudo-	emptied and can re-filled with data. The Link will no longer send any data inserted	before the time of the reset.

To prevent that data is written into a full FIFO there is a register which shows the	number of free record spaces in the FIFO (s. 1.1.):

For the representation of the FIFO depth only 11 bits are necessary but the whole	register is reserved for it. De facto the bits 31 down to 12 are unplaced. The writing into	a full FIFO does not cause any harm on hardware or system but the data is lost though.

Although this address is marked as write-only it is able to read the last written record via	a read request.

3.2. Receiving (RX)
Via SpaceWire received data is written gradually into the RX FIFO and can be read by	the CPU. (s. 2.2.)

The FIFOs width is nine bits wide which are divided as follows:
Bit 8 : flag bit (1 : Process ID/EOP/EEP, 0 : data)
Bit 7 – Bit 0 : received data byte (0xFF for EOP, 0xFE for EEP)

In depth, 2049 records fit into the FIFO. Is the FIFO completely full and is then a read-	request followed by a write-request executed the write-request may fail. This is due to	technical reasons and can be circumvented by reading at least two elements out of the	FIFO under that circumstances.

Data read out of the FIFO contains nine valid bits (0x0000_0xvv), where x is either 0x0	or 0x1 and vv any data byte. Is x equal to 0x1, vv must be differentiated: If vv = 0xFF it	is an EOP (End of Packet), for 0xFE it is an EEP (Error End of Packet) and otherwise it	is a process id (0x00 – 0xFD, 0x – 253) or a logical address of a the SpaceWire packet.

Reset of the FIFO is done via the reset of the Link (or the Logic) (via a GPIO). Thereby	the FIFO is pseudo-emptied and can be re-filled with data. The Processing System is	then not able to read data that was received before the time of the reset.

To prevent that data is read out of an empty FIFO there is a register which shows the	number of available elements currently stored in the FIFO (s. 1.2.):

For the representation of the number of elements stored in the FIFO are just 11 bits	necessary but the entire register is reserved for it. So de facto the bits 31 down to 12	are unplaced.

If the FIFO is empty the last valid element stays at its output as long as new data is	written into the memory. So its recommended to include the elements register (s. 1.2.).

3.3. Register (REG)
The width of the entire register is 32 bits. The placement of individual bits varies	depending on the address.

3.3.1. - Link-Configuration: (read/write) — 0x0000_0000

autostart

unbelegt

linkstart
linkdis

linkdis	Deactivates the link, receiving and transmitting of message is no longer possible. Default value: 1. / 1 : Deactivates link (linkstart/autostart will be overwritten) / 0 : Link is not deactivated
linkstart	Activates the link. Connection attempts are regularly made with the opposite entity. An active attempt is made to establish a connection with the opposite party. A connection attempt is made at regular intervals. Default value: 0. / 1 : Link starten / 0 : Link nicht starten
autostart	Activates the link. It is not tried to make a connection attempt with the opposite entity. But on connection attempts outgoing of the opposite entity is reacted cooperatedly. Standardwert: 0. / 1 : Automatischer Verbindungsaufbau aktiviert / 0 : Automatischer Verbindungsaufbau deaktiviert

3.3.2. - Transmit Rate (read/write) — 0x0000_0004

unbelegt
txdivcnt

txdivcnt<7:0>	Skalierungsfaktor minus 1. Wird benutzt um die Sendebitrate aus dem Transmit-Takt abzuleiten. Standardwert: 0x01.

3.3.3. - Time-Codes (ausgehend) (read/write) — 0x0000_0008

unbelegt
Control Flag
 unbelegt
Counter Value

Counter Value <5:0>	Wert des Time-Codes, der zur Synchronisierung benutzt wird (Wertebereich: 0-63). Standardwert: 0b00000.
Control Flag <1:0>	Flag des Time-Codes. Standardwert: 0b00.

3.3.4. - Time-Codes (eingehend) (read only) — 0x0000_000C

unbelegt
Counter Value
Control Flag
unbelegt

Counter Value <5:0>	Wert des Time-Codes, der zur Synchronisierung benutzt wird (Wertebereich: 0-63)
Control Flag <1:0>	Flag des Time-Codes. (Standard: 0b00)

3.3.5. - Link-Status (read only) — 0x0000_0010

unbelegt
unbelegt
unbelegt

rxfull
txfull

rxhalff
errcred
running
txhalff

rxempty
erresc
connecting
txempty

started
errpar

errdisc

started	Zeigt an, ob der SpaceWire Link im started-Zustand ist. (Nicht verbunden, aber bereit eine Verbindung aufzunehmen)
connecting	Zeigt an, ob der SpaceWire Link im connecting-Zustand ist. (Verbindungsaufnahme im Gange)
running	Zeigt an, ob der SpaceWire Link mit einem anderen Link erfolgreich verbunden und lauffähig ist.
errdisc	Zeigt an ob ein Disconnect entdeckt wurde. Der Link cleart diesen Fehler automatisch und versucht eine erneute Verbindungsaufnahme.
errpar	Zeigt an ob ein Paritätsfehler während einer Datenübertragung entdeckt wurde. Der Link cleart diesen Fehler automatisch und versucht eine erneute Verbindungsaufnahme.
erresc	Zeigt an ob ein Escape-Fehler während der Datenübertragung entdeckt wurde. Der Link cleart diesen Fehler automatisch und versucht eine erneute Verbindungsaufnahme.
errcred	Zeigt an ob ein Credit-Fehler entdeckt wurde. Der Link cleart diesen Fehler automatisch und versucht eine erneute Verbindungsaufnahme.
rxempty	Zeigt an ob der interne Eingangs-FIFO des Links (nicht der RX FIFO unter 1.2.) nicht befüllt ist.
rxhalff	Zeigt an ob der interne Eingangs-FIFO des Links (nicht der RX FIFO unter 1.2.) zur Hälfte befüllt ist.
rxfull	Zeigt an ob der interne Eingangs-FIFO des Links (nicht der RX FIFO unter 1.2.) vollständig befüllt ist.
txempty	Zeigt an ob der interne Ausgangs-FIFO des Links (nicht der TX FIFO unter 1.1.) nicht befüllt ist.
txhalff	Zeigt an ob der interne Ausgangs-FIFO des Links (nicht der TX FIFO unter 1.1.) zur Hälfte befüllt ist.
txfull	Zeigt an ob der interne Ausgangs-FIFO des Links (nicht der TX FIFO unter 1.1.) vollständig befüllt ist.

4. Steuerung

4.1. Inbetriebnahme
Um den Link in Betrieb zu nehmen sind folgende Schritte erforderlich:
1. Herstellen einer physischen Verbindung der SpaceWire-Verbindungen (spw_do,	spw_so und spw_di, spw_si) zu einem externen SpaceWire-Link.
2. Aktivieren des Interfaces:
2.1. Durchführen eines initialisierenden Resets sowohl der Logik wie auch	des AXI Busses (Reihenfolge irrelevant) über mindestens fünf Taktzyklen des	langsameren Taktes der beiden beteiligten (Bsp.: AXI Clock: 50 MHz; Logik	Clock: 100 MHz; mindestens 100 ns Reset durchführen)
-- Kann ggf. entfallen. --
2.2. Schreiben des Wertes 0x01 in das Transmit-Rate-Register.
2.3. Schreiben des Wertes 0x06 in das Link-Konfigurationsregister.
2.4. Warten bis Verbindungsaufnahme hergestellt wurde. Feststellbar ist dies	über entsprechendes Interrupt oder über das Statusregister.
3. Ab jetzt können Daten gem. Kap. 2 verschickt und empfangen werden.

4.2. Steuerung
Um Daten in den TX-FIFO zu schreiben, genügt es, einen Zeiger auf dessen Adresse	(s. 1.1.) zu richten und diesem entsprechend Daten zuzuweisen. Diese Transaktion	wird intern über den AXI-Bus abgewickelt.

Selbes Vorgehen ist beim RX-FIFO notwendig, nur das hier Daten gelesen werden	sowie der Zeiger dereferenziert wird. Dadurch wird auch – sofern sich mehr als ein	Element im FIFO befindet – das nächste Elemente an den FIFO Ausgang geladen.

Ankommende, gültige Time-Codes werden mittels eines Interrupts an die CPU	gemeldet. Es muss also eine entsprechende ISR (Interrupt Service Routine)	geschrieben und am Processing System (PS) registriert werden. Die Werte des Time-	Codes sind dann über das entsprechende Register (s. 1.3.) abrufbar.

Sowohl der TX als auch der RX Zweig sind über AXI4-Full angebunden und	unterstützen Burst Transfer. (Bis zu 255 Datenworte in einer Transaktion	lesen/schreiben). Durchgeführt werden kann dies allerdings ausschließlich über einen	DMA Controller und nicht über Programmcode.

Soll ein Time-Code verschickt werden, ist es zuerst nötig, die entsprechenden Werte	innerhalb des dafür zuständigen Registers (s. 1.3.) zu schreiben. Danach wird der dafür	vorgesehene GPIO auf HIGH gesetzt. So wie das Link-Interface eine steigende Flanke	dieses GPIOs erkennt, wird mittels der Daten im Register (s. 1.3.) ein Time-Code	generiert und priorisiert verschickt. Dabei genießt es Vorrang gegenüber den Daten im	Tx-FIFO. Allerdings kann durch den Link gerade ein Datenwort verschickt werden, was	die	Versendung des Time-Codes um einige Takte verzögern kann. Wichtig ist, den	GPIO nach diesem Prozess wieder auf LOW zu setzen.

4.3. Außerbetriebnahme
Um den Link zu deaktivieren oder abzuschalten genügt es, in das Link-	Konfigurationsregister den Wert 0x0000_0001 zu schreiben. Damit wird linkdis aktiviert,	welche alle anderen Einstellung innerhalb dieses Registers überschreibt. Um beide	FIFOs zurückzusetzen, müssen sowohl das AXI-Interface als auch das Link-Interface	über einen Zeitraum von mindestens 5 Taktzyklen resettet werden.